LDATA

PURPOSE :       LDATA reads an FCS histogram file and writes its raw data
                segment to the screen or to an ASCII file.  It is used when
                it is convenient to have histogram data in a human readable
                format, or when the data needs to be read by a standard
                analysis or statistics program.


USAGE :         LDATA <inputfile> [<outputfile>]


SYNOPSIS :      The output format from a one parameter histogram is simply
                each channel count in text form, separated by a single space,
                with 16 values per line.  A 256 channel histogram therefore
                produces 16 lines of output, while a 1024 histogram produces
                64 lines.

                A two parameter histogram is written with one row of channels
                per row of output.  This puts the origin of the histogram at
                the top left of the screen or output file and the first
                parameter on the x-axis and the second on the y-axis.  Values
                are separated by single space characters.  This means that
                for standard 64 channel histograms with fewer than 65536
                events per channel, each line might be as long as 
                (5 + 1) * 64 = 384 characters.

                If no output file is specified, output will be written to
                the computer screen.